## Slide 1: Microcontroller Assignment no 7
Sneha Deo
NBN Sinhgad School Of Engineering

## Slide 2: Assignment – 16 bit x 8 bit Multiplication
Logic
16 bit number = 1234H
8 bit number = 10H
Multiplication of 1234×10
Step 1: 34 x 10= 0340H
Keep 03 as carry and 40 as the lower byte of the answer.
Step 2: 12 x 10= 0120H
Step 3: Add the carry 0120+ 03=0123
Therefore the answer is 012340

## Slide 3: Example Explained
1
4
3
2
1
0
0340
03-Carry
40-Answer
16 Bit
8 Bit
0120 +
=0123 +40 (From Previous Multi.) =12340
=0123

## Slide 4
Algorithm
Load the lower byte of the 16 bit multiplier into accumulator A and 8 bit multiplicand into register B
Multiply them using instruction MUL AB
Store lower byte of product in internal register (R0)
Store the higher byte of product in one of general purpose register (R1)
Get higher byte of 16 bit multiplier into accumulator and 8 bit multiplicand into register B
Multiply them using instruction MUL AB.
Add lower byte of the product with higher byte of result (R1) produced after first multiplication.
Store the second byte of result into internal register (R2).
Add carry with the higher byte of result generated after second multiplication and store it as first (Most Significant) byte of product into register (b) .
Assignment – 16 bit x 8 bit Multiplication